## Slide 1: Electrostatic Tractor Supercharging in Cislunar Space
Landon Holligan

## Slide 2
Space Debris Problem
Near Earth orbits are crowded with hundreds of thousands of pieces of debris
With more mission objectives pointing toward Cislunar Space, space debris is a major concern
Highlights a need for safe debris removal/mitigation strategies

## Slide 3: Electrostatic Tractor Basics
Servicer equipped with an electron beam
Servicer charges positive and target charges negative
Creates tugging force on target

## Slide 4: Intro To Plasma Wakes
Spacecraft “pushes” and absorbs ions as it flows through plasma
Occurs in mesothermal plasma where:
-
Ions
-
+
+

## Slide 5: Supercharging Concept
Supercharging occurs when
Must occur inside a plasma wake so target does not collect ions
Generates larger potential difference, creating stronger tugging forces
T
SC
Target in Servicer’s Wake.
Electron Beam not Fully Recollected by Servicer
>
-1.02 kV
297 V

## Slide 6: Cislunar Plasma Region

## Slide 7: Objective:
Build on our lab’s findings to prove that supercharging can occur and characterize possible conditions.
Steps
Use SPIS and MATLAB to characterize wakes
Use SIMION and MATLAB to find beam width of electron gun
Use SPIS to model supercharging

## Slide 8: SPIS
3D plasma-interaction solver
Able to model complex spacecraft geometry
Detailed sheath/wake modeling

## Slide 9
0 V Target
-5 kV Target
-10 kV Target
-15 kV Target
-20 kV Target
1 kV Servicer, 4m Separation
0 V Target
-5 kV Target
-10 kV Target
-15 kV Target
-20 kV Target
10 kV Servicer, 4m Separation
SPIS Wake Figures
Much Larger Wake
Fully Collapsed

## Slide 10: SPIS Current Results

## Slide 11: SIMION
Servicer
Target
Tracks particle trajectories
Can model electron beam spread
Analyzes impacts and recollection

## Slide 12: SIMION Results
Looking for balance between electron impacts and recollection

## Slide 13: Proposed Beam Width
18.4°
Half Angle

## Slide 14: Supercharging Validation
Servicer does not recollect all the emitted electrons
-3 kV
3.32 kV
To verify supercharging in a plasma environment, we start with a potential difference equal to the beam energy
Initial Parameters:
71.2% higher than

## Slide 15: Applied Supercharging
Initial Parameters:
Possible to charge SC and target to equilibrium with electron beam, then maintain this potential difference at lower
-9.4 kV
2.61 kV
In wake
2.06 kV
358 V
Not in wake
Objects repel eachother

## Slide 16: Additional Charging Application
Initial Parameters:
After charging to equilibrium with a beam, we can point the beam away from the target and continue charging
Wake has not collapsed
Beam emitted away from the target
-9.3 kV
4.47 kV
Increased by 44.14 %

## Slide 17: Summary
3. It is possible to maintain a significantly higher potential difference than the energy of the beam if the target stays in the wake
1. Supercharging must occur inside of a plasma wake
4. It is possible to continue charging passed equilibrium by pointing the beam away from the target
2. A wider beam width, to an extent, provides better supercharging

## Slide 18: Next Steps
Explore supercharging in additional mesothermal regions (Cislunar, LEO)
Apply supercharging concepts to more realistic geometries
Optimize beam width, separation distance and beam energy and current
Explore uses in active charge or attitude control

## Slide 19: References
[1] Strain, Daniel. “Space tractor beams may not be the stuff of sci-fi for long.” Phys.org, June 1, 2023. https://phys.org/news/2023-06-space-tractor-sci-fi.html
[2] European Space Agency. “Space debris - evolution in pictures.” ESA. https://www.esa.int/About_Us/ESOC/Space_debris_-_evolution_in_pictures
[3] Case, Nathan A. Solar Wind-Magnetosphere Interactions: A Statistical Analysis of Spacecraft Measurements. PhD thesis, Lancaster University, April 2014. https://doi.org/10.13140/2.1.2588.8321
Acknowledgements
Kaylee Champion, Graduate Student, University of Colorado Boulder
Hanspeter Schaub, Faculty Advisor, University of Colorado Boulder
Discovery Learning Apprenticeship, University of Colorado Boulder
Sharon Anderson, University of Colorado Boulder
U.S. Air Force Office of Scientific Research (AFOSR) under grant FA9550-23-S-0570

## Slide 20
Questions?